## Slide 1: Solved Tutorial Questions
Example of Self Inductance
1. A hollow air cored inductor coil consists of 500 turns of copper wire which produces a magnetic flux of 10mWb when passing a DC current of 10 amps. Calculate the self-inductance of the coil in milli-Henries.
Recall that
Therefore

## Slide 2
2 Calculate the value of the self-induced emf produced in the same coil after a time of 10mS.
Recall that
Therefore,
Example of Mutual Inductance
3. Two inductors whose self-inductances are given as 75mH and 55mH respectively, are positioned next to each other on a common magnetic core so that 75% of the lines of flux from the first coil are cutting the second coil. Calculate the total mutual inductance that exists between the two coils.

## Slide 3
4. When two coils having inductances of 5H and 4H respectively were wound uniformly onto a non-magnetic core, it was found that their mutual inductance was 1.5H. Calculate the coupling coefficient that exists between.

## Slide 4
An air cored coil of self inductance L has N turns of fine insulated copper wire wound on a former of cross section area A. If the area and number of turns are doubled and the core is a medium of relative permeability 1000, the self inductance of the coil will be
(a) 8000 L (b) 4000 L (c) 8×10–3 L (d) 4×10–3 L (e) L
Sol.
Self inductance of a coil is directly proportional to the area of cross section, relative permeability of the core and the square of the number of turns. The answer therefore is 8000 L.
Answer (a)
2. A straight air cored solenoid has length 1 m, area of cross section 10 cm2 and total number of turns 2000. If a current of 1 A flowing in it is reversed in 0.1 s, the average emf induced in it will be nearly
(a) 100V (b) 10 V (c) 1 V (d) 0.5 V (e) 0.1 V
Sol. The emf induced is given by ε = –L(dI/dt),
where dI is the change in current in the time dt and L = μ0n2Aℓ where ‘ℓ’ is the length of the solenoid, ‘A’ is its cross section area, ‘n’ is the number of turns per metre and μ0 is the permeability of air (or free space) which you must remember as 4π×10–7.
Ignoring the negative sign which is because of Lenz’s law, we have
ε = μ0n2Aℓ (dI/dt)
Substituting, ε = 4π×10–7×(2000)2×(10×10–4)×1×[1– (–1)]/(0.1) volt.
Note that the change in the current is 2 A ( from 1 A to –1 A) since the current is reversed.
Therefore, ε = 0.1 (nearly).
Answer 0.1 V (e)

## Slide 5
In the circuit shown, the switch S is kept closed so that the current flowing in the circuit is the final steady value. When the switch S is opened, the time constant for the decay of current in the inductance is
(a) L/R (b) L/5R (c) 5L/4R (d) 4L/5R (e) L/3R
The current decays through the resistors R and 4R in series with L and therefore the time constant is L/(R+4R) = L/5R.
Answer (b)
In the above question, suppose the resistance 4R is disconnected and is then connected between the inductance L and the negative terminal of the battery. The switch S is kept closed. If the switch is opened, the time constant for the decay of current in L is
(a) L/R (b) infinity (c) zero (d) L/5R (e) 5L/4R
This is a simple case which may however generate confusion in your mind. Note that when you open the switch, the resistance in series with L is infinite and the time constant will be L/∞ = 0.
Physically, the current becomes zero abruptly since there is no conducting path for the current to flow.
[Discharging of a charged capacitor through a resistor is an easy thing since the capacitor can retain the charge during the small time during which the capacitor is disconnected from the charging battery and then connected to the resistor, using a charge-discharge key. In the case of the LR circuit, for studying the current decay pattern, after establishing the steady final current through the circuit, you have to short circuit the leads connected to the battery and immediately disconnect the battery so that the battery is not damaged].
Answer (c)

## Slide 6
5. vertical conductor. The coil and the straight conductor are contained in the same vertical plane. The mutual inductance between the coil and the straight conductor is
(a) μ0 nr2/2πd (b) π μ0 nr2/2d (c) μ0 nr2/2 (d) μ0 nr2/2π2d (e) μ0 nr2/2d
The mutual inductance is given by
M = Ф/I where I is the current in the straight conductor and Ф is the magnetic flux through the coil.
Since the coil is small, the magnetic field produced at the coil by the current in the straight conductor can be assumed to be constant over the entire area of the coil so that
Ф =nBA = n(μ0I/2πd)(πr2) Therefore, M = μ0 nr2/2d
Answer (e)
6. A long straight solenoid of cross section area10 cm2 has 10 turns per cm. A short 50 turn coaxial coil of cross section area 2 cm2 is fixed inside the solenoid at the middle. The mutual inductance of the solenoid and the coil is (in micro henry)
(a) 400 (b) 40 (c) 4π (d) π (e) ) 0.4π
Mutual inductance between an infinitely long straight solenoid and a short secondary coil placed coaxially inside at the middle is given by
M = μ0nNA where μ0 is the magnetic permeability of free space (or air), n is the number of turns per metre of the solenoid, N is the total number of turns in the secondary coil and A is the cross section area of the secondary coil. (If the secondary coil is outside the solenoid, the cross section area of the solenoid will appear in place of the area of the secondary coil).
[Note that the mutual inductance as given by the above expression is the magnetic flux (linked with the secondary coil) per unit current in the solenoid: M = NBA where B is the magnetic field (μ0n×1) produced by unit current in the solenoid]
Substituting for the known quantities in the expression for mutual inductance, we have
M = 4π×10–7×1000 ×50 ×(2×10–4) = 4π×10–6 H = 4π μH.
Answer (c)

## Slide 7
7. The secondary coil in the above question is moved with uniform velocity coaxially over a distance of 5 cm in 2 seconds when a current of 2 ampere flows through the solenoid. The emf induced in the coil during the motion is
(a) 200π μV (b) 100π μV (c) 20π μV (d) 10π μV (e) zero
No emf will be induced in the coil since the same flux is linked with the coil throughout its motion and there is no flux change.
Answer (e)
8. In question No.1, suppose the solenoid carries a current of 4 A. If this current is switched off in 100 ms, the emf induced in the secondary coil will be
(a) 0.2π μV (b) 0.4π μV (c) π mV (d) 0.08π mV (e) 0.16π mV
We have ε = –M(dI/dt) = = 4π×10–6 [(4 – 0)/(100×10–3)] = 160π×10–6 volt = 0.16π mV.
Answer (e)
9. A battery of emf V volt is connected in series with a coil of inductance L and resistance R at the instant t = 0. The current in the circuit when t = 2τ where τ is the time constant of the circuit is (base of natural logarithm = e)
(a) (V/R)[1– (1/e2)] (b) (V/R (1/e2) (c) (V/R)[1– (1/e)] (d) (V/R)(1/e)] (e) 2e(V/R)
The expression for the growth of current (with time) in an LR circuit is I = I0[1– e–Rt/L] where I0 is the final steady (maximum possible) current which is equal to V/R.
The time constant of the LR circuit is L/R. After 2 time constants, the current will be
I = I0[1– e–R× 2(L/R)/L] = (V/R) [1– e– 2] = (V/R)[1– (1/e2)]
Answer (a)

## Slide 8
10. Self induced e.m.f is sometimes also known as
(a) induced e.m.f (b) deduce e.m.f (c) back e.m.f
(d) both a and b (e) none of the above
Answer (c)
11. Change of current of 1 As-1 causes e.m.f of 1 V to be equal to
(a) 1 henry (b) 1 volt/m (c) 1 ampere (d) 1 joule (e) 1 N
Answer (a)
12. Changing current in one coil induces e.m.f in another this phenomena is known as
e.m.f (b) induced e.m.f (c) self induction (d) mutual induction (e) Lenz law
Answer (d)
13. Negative sign of equation of self induction shows that
(a) deduce e.m.f (b) it maintains change (c) it opposes change
(d) induced e.m.f (e) increase the e.m.f
Answer (c)